## Slide 1: SDN

## Slide 2: Agenda
About me
Requirements of Software-Defined Networking (SDN)
What is SDN
SDN killer application - Network Function Virtualization NFV
Trema - an OSS SDN controller
Questions

## Slide 3: Requirements of SDN
Internet protocol suite - many independent layers, lots of protocols, well defined standards.
  Application layer (BGP, and other management protocols)
  Transport layer ( Best-effort delivery TCP, UDP others)
  Internet layer (IP, ICMP, IPsec)
  Link layer (OSPF, ARP Tunnels, Media access control (Ethernet))
Defined - use software to define abstractions to express the network in simpler terms
Network A network as a service - a cloud computing term that provides transport connectivity to users.
Users can use NaaS to implement custom forwarding decisions based on application needs.
Notes: Difficult to introduce a new control mechanism - increased complexity. There is no control plane abstraction. For example applications can choose TCP or UDP depending on real-time constraints imposed to achieve what is required best.

## Slide 4: A router a vital network element
a typical router - a soup of protocols, all three layers implemented in one box, lots of decision logic.
Management plane: CLI/GUI
  Control plane: static routes, OSPF(Open Shortest Path), Neighbor, link, ip routing tables
  Data plane: forwarding table
Some protocols like BGP require manual configuration.
A misconfiguration may have a significant impact on the network.

## Slide 5: From the user perspective
Many user traffic patterns
to deal with such traffic patterns
  middleboxes, load balances, firewalls, network address translators
  user mobility, tenant network isolation
  seamless device connection to network
  traffic analytics
Notes: All the above complicated our network requirements and it is believed that configuring such networks would be cumbersome and error prone task for network operators.

## Slide 6: SDN definition
Provides a vendor agnostic programming interface to program the network devices.
Programmability is one of the main properties of SDN.
Programmability achieved by an abstracted control plane.
  decides of how to handle the traffic
  defines “network programs” that manage network elements providing rich applications with enhanced functionality.
Decisions of control plane directed as instructions to data plane executed by the forwarding module.
Applications use a global view to interact with the control plane.

## Slide 7: Alternative SDN Implementation
Linecard forwarding model:
  Supports OpenFlow plus x86 (and perhaps GPU)
Switch configuration model:
  Supports JVM (controller can download code)
NOS distributed state model:
  key/value store of state with data model
  Data model enforces some application-specific constraints.
Mainly an illustration of a richer form of SDN
  Enables features to emerge in software, migrate to H/W

## Slide 8: Are we done yet?
This approach requires control program or operator to configure each individual network device.
That is more complicated than it should be!
NOS eases implementation of functionality.
  but not specification of functionality.
How can we provide abstractions that are more meaningful to operators and control programs?

## Slide 9: Simplifying Specification via Abstraction
Give control program abstract view of network
  Where abstract view is function of global view
Then control program is abstract mapping
  - Abstract configuration = F(abstract view)
Model just enough detail to specify goals
  - Don’t provide information needed to implement goals

## Slide 10: One Simple Example: Access Control
Full Network View
Abstract Network View

## Slide 11: More Detailed Model
Service model can generally be described by a table pipeline.
Packet In
L2
L3
ACLs
Packet Out

## Slide 12: How to implement this?
Create table pipelines in virtual space (L2, L3, ACL).
Distribute pipeline operations over network of physical hardware. (physical switches)

## Slide 13: SDN V2
Control program
Abstract Network View
Nypervisor
Global Network View
Network Operation System
Network Elements

## Slide 14: Three Network Interfaces
Forwarding interface
  Provides flexible abstract forwarding model
Global network view
  Shields higher layers from state dissemination/collection
Abstract Network View
  Shields control program from details of physical network.

## Slide 15: From SDN to clean state architecture
These are the basic abstractions that underlie SDN
Are abstractions only relevant to network control?
What about more general architectural questions?
What problems do we want abstractions to solve?
  Architectural rigidity.
How can we make the architecture evolvable?

## Slide 16: Why is current architecture rigid?
IP is central component of architecture
IP is embedded in interdomain routing
  and interdomain routing is hard to change
IP is embedded in applications (via API)
  and hard to change all applications
Therefore very hard to change all IP.

## Slide 17: Current Internet
Application
Network Stack
  IP
Domain
  BGP
Rest of internet
Architecture is very rigid

## Slide 18: Insert Two Architectural Abastraction
Control program
Abstract Network View
Nypervisor
Global Network View
Network Operation System
Network Elements