## Slide 1: Software Defined Network

## Slide 2: Agenda
About me
Requirements of Software-Defined Networking (SDN)
What is SDN
SDN killer application - Network Function Virtualization NFV
Trema - an OSS SDN controller
Questions

## Slide 3: About me
My full name: Nick Karanatsios
Full-time employee of NEC Engineering Ltd.
Participation on OSS project(s).
25+ years of programming experience.
My favorite programming languages - Ruby and Objective C.
Involved in OpenFlow development projects nearly since it’s inception.

## Slide 4: Need for SDN?
Computer networks are complex and hard to manage.
Internet protocol suite - many independent layers, lots of protocols, well defined standards.
  Application layer (BGP, and other management protocols)
  Transport layer ( Best-effort delivery TCP, UDP others)
  Internet layer (IP, ICMP, IPsec)
  Link layer (OSPF, ARP Tunnels, Media access control (Ethernet))
Application layer
Transport layer
IP layer
Link layer
Internet
Protocol
Suite
Notes: Difficult to introduce a new control mechanism - increased complexity. For example applications can choose TCP or UDP depending on real-time constraints imposed to achieve what is required best. On the next slide we focus on one of the most common device router.

## Slide 5: Many kind of equipment
Routers, switches, middleboxes (firewalls, network address translators, server load balances, intrusion detection systems)
Routers and switches run complex distributed control software typically closed and proprietary.
a soup of protocols, all three layers implemented in one box, lots of decision logic.
Implemented network protocols undergo years of standardization and interoperability testing.
Management plane: CLI/GUI
  Control plane: static routes, OSPF(Open Shortest Path), Neighbor, link, ip routing tables
  Data plane: forwarding table
Some protocols like BGP require manual configuration.
Configuration interfaces vary between vendors.
A misconfiguration may have a significant impact on the network.
Router/Switch
Management plane
CLI/GUI
Control plane
OSPF
data plane
forwarding table
IP routing table
static routes
link state table
neighbor table
Notes: At least you have Open Shortest Path/ Policy based routing
Management/Policy plane

## Slide 6: User requirements
end-to-end quality of service assurance
easy access to network from any user device
User mobility
isolation of user typically found in cloud system while maximizing resource sharing
higher bandwidth requirements with introduction and support of 3D high definition content.
to deal with such diverse traffic patterns
  middleboxes, load balances, firewalls, Carrier Grade NAT (CG-NAT), intrusion prevention system (IPS), intrusion detection system (IDS), encryption and compression engines.
Notes: All the above complicate our network requirements and it is believed that configuring such networks would be cumbersome and error prone task for network operators.

## Slide 7: What is SDN?
SDN analogous to any operating system. SDN’s OS is called Network OS(NOS).
NOS separates abstracts and centralizes the control of the network (which decides how to handle the traffic) from the underlying data forwarding plane (which forwards traffic according to decisions that the control plane makes).
NOS segregates applications from knowing low level details to program the network.
Forwarding infrastructure - a list of sparse network elements refer to as switches or as network elements.
Network OS
Forwarding Infrastructure
Control
Plane
Data
Plane
App
App
App
Notes: A single control plane control multiple data planes via a well
In the simple cases switches would not exchange any control information between them. In other cases switches may be more advance boxes with routing and tunneling capabilities. Switches may also be aggregation switches that pass traffic to a core network. The core network could be a non SDN network. For example it could be an IP/MPLS network.

## Slide 8: what is SDN?
Applications use the northbound API to interact with the SDN control plane.
SDN control plane hosts specific network modules and other more general modules.
Control plane to data plane interaction is governed by the southbound API.
OpenFlow is one of the most used control protocol but not the only one.
App layer
App
App
App
Topology
Discovery
Traffic
Engineering
Mobility
SDN Control S/W
NBI API
router
switch
Data Plane
SBI API
Label
Distribution
Notes: NBI - NorthBound API not standardlized most likely to be RESTful. SouthBound API is OpenFlow other protocols could also be used.
Topology discovery can be thought as an embedded application.
Mention the ForCES RFCxxxx.

## Slide 9: SDN layers
Clean separation b/n application and control layer.
Logically centralized control layer responsible for creating network services for applications to use.
Infrastructure layer executes actions on behalf of the control layer.
Business Applications
Business Applications
Business Applications
Application
Layer
Control
Layer
Business Applications
Business Applications
Network Services
Infrastructure
Layer
Network Element
Network Element
Network Element
OpenFlow
API

## Slide 10: SDN Control Layer Views
NOS distributed state model - physical topology and state information into global network view.
NOS embedded applications create a simplify view of the network - abstract network view.
Abstract/virtual network view example access control list (ACL).
Control
Layer
Network OS
Global NetworkView
Abstract Network View
Embedded Applications

## Slide 11: Three Network Interfaces
Abstract Network View
  Shields control program from details of physical network.
Global network view
  Shields higher layers from state dissemination/collection.
Forwarding interface
  Provides flexible abstract forwarding model.

## Slide 12: OpenFlow
OpenFlow basic idea is that routers are dumb boxes and routing information is to be downloaded from a central controller.
Controller takes in configuration network and other information and outputs a different decision table (flow) for each router.
Packets are selected by port, MAC address, IP address address and table indicates what action to take; drop, forward or modify and then forward.
OpenFlow is a traffic engineering tool - can program latency sensitive traffic to take the fastest path while bulk flows can the take the cheapest path.
OpenFlow is also a NAT - it can rewrite packets
OpenFlow is also a firewall it can drop packets
OpenFlow can also implement ECMP(Equal-cost multi-path) or any other load balancing scheme.

## Slide 13: Alternative SDN Implementation
Linecard forwarding model:
  Supports OpenFlow plus x86 (and perhaps GPU)
Switch configuration model:
  Supports JVM (controller can download code)
NOS distributed state model:
  key/value store of state with data model
  Data model enforces some application-specific constraints.
Mainly an illustration of a richer form of SDN
  Enables features to emerge in software, migrate to H/W

## Slide 14: Are we done yet?
This approach requires control program or operator to configure each individual network device.
That is more complicated than it should be!
NOS eases implementation of functionality.
  but not specification of functionality.
How can we provide abstractions that are more meaningful to operators and control programs?

## Slide 15: Simplifying Specification via Abstraction
Give control program abstract view of network
  Where abstract view is function of global view
Then control program is abstract mapping
  - Abstract configuration = F(abstract view)
Model just enough detail to specify goals
  - Don’t provide information needed to implement goals

## Slide 16: One Simple Example: Access Control
Full Network View
Abstract Network View

## Slide 17: More Detailed Model
Service model can generally be described by a table pipeline.
Packet In
L2
L3
ACLs
Packet Out

## Slide 18: How to implement this?
Create table pipelines in virtual space (L2, L3, ACL).
Distribute pipeline operations over network of physical hardware. (physical switches)

## Slide 19: SDN V2
Control program
Abstract Network View
Nypervisor
Global Network View
Network Operation System
Network Elements

## Slide 20: Three Network Interfaces
Forwarding interface
  Provides flexible abstract forwarding model
Global network view
  Shields higher layers from state dissemination/collection
Abstract Network View
  Shields control program from details of physical network.

## Slide 21: From SDN to clean state architecture
These are the basic abstractions that underlie SDN
Are abstractions only relevant to network control?
What about more general architectural questions?
What problems do we want abstractions to solve?
  Architectural rigidity.
How can we make the architecture evolvable?

## Slide 22: Why is current architecture rigid?
IP is central component of architecture
IP is embedded in interdomain routing
  and interdomain routing is hard to change
IP is embedded in applications (via API)
  and hard to change all applications
Therefore very hard to change all IP.

## Slide 23: Current Internet
Application
Network Stack
  IP
Domain
  BGP
Rest of internet
Architecture is very rigid

## Slide 24: Insert Two Architectural Abastraction
Control program
Abstract Network View
Nypervisor
Global Network View
Network Operation System
Network Elements